Table of Contents

JUMPER & CONNECTOR LOCATION DIAGRAM	A

CHAPTER 1   INTRODUCTION	2

1-1 SYSTEM FEATURES	3

1-2 CHECK LIST OF THE PACKING	4

CHAPTER 2   INSTALLATION	5

2-1 INSTALLATION PROCEDURES 	5

2-2 CPU INSTALLATION	6

2-3 SYSTEM MEMORY INSTALLATION	11

2-4 SRAM INSTALLATION	13

2-5 OTHER JUMPERS AND CONNECTORS 
       DESCRIPTION 	14

2-6 IDE DRIVER INSTALLATION	19

CHAPTER 3   AWARD BIOS SETUP	20

3-1 UPDATE BIOS PROCEDURES	21

3-2 AWARD SYSTEM BIOS CONFIGURATION SETUP	22

APPENDIX A 	46

CHAPTER 1 INTRODUCTION

This manual introduces how to configure the ATC-2000 mainboard for different environments. It's an overview of the layout and features of the mainboard, and also provides

information for you to change the configuration or system environment.

This manual is divided into two sections :

PART ONE includes page A which contain layout diagram of

the mainboard. Please refer it when you configure the system.

PART TWO includes three chapters as following:

Chapter 1 is an overview of the mainboard features and packing

contents of the mainboard.

Chapter 2 describes how to upgrade and to change hardware

configurations such as memory size, CPU type, and lists of

jumper settings and connectors.

Chapter 3 is the user's guide of AWARD BIOS setup utility,

and Flash ROM BIOS update procedure. The menu showed in

this chapter are default settings.

Your system dealer will set up the mainboard according to your demand of computer. It means that the current settings of your mainboard's current setting may not be the same as the defaults shown in this user's manual.  If you need to change your

configuration, please ask your dealer firstly, be sure this will not

against your system warranty. Or ask for your dealer to do it for you.

REMARK

Intel  is a registered trademark of Intel Corporation.

MS-DOS is a registered trademark of Microsoft Corporation.

All other brands and product names are trademarks registered trademarks of their respective companies.

1-1 SYSTEM FEATURES

P54C, P55C Pentium level CPU operating at 75 MHz to 200MHz with 321-pin ZIF socket 7 and scalability to accept processor in the future.

INTEL 82430HX PCIset.

Using four 72-pin SIM sockets, provides two banks of 64-bit wide path up to 256MB addressing page mode DRAMs.

Supporting all types of DRAM included ECC (Error Checking and Correcting) or parity, EDO (Extended Data Out), BEDO (Burst EDO), or FPM (Fast Page Mode).

Supporting four PCI bus master revision 2.1, 5V interface compliance and four 16-bit ISA slots.

Dual Master IDE connectors support up to four devices in two channels for connection of high capacity hard disk drive, CD-ROM drive, tape backup etc..

Supporting the USB (Universal Serial Bus) connector.

"True" Green power management for CPU stop clock state.

AT style keyboard connector and PS/2 mouse connector.

Winbond 83877 high-speed Multi-I/O chipset:

Supporting Infrared transfer (IrDA TX/RX) connection.

One FDC port supports two devices up to 2.88MB

Two 16550A fast UARTs compatiable serial ports

One EPP/ECP mode parallel port

Hardware Dimension is 220mm x 280mm (8.66" x 11.02") with four layers designed.

1-2 CHECK LIST OF THE PACKING

The mainboard comes securely packed in a durable box and shipping carton. If any of the above items are missed or damaged, please contact your supplier.

Each mainboard containing:

Q'TY     	Description

1         Mainboard 	: ATC-2000.

1	Diskette	: Enhanced IDE driver (3.5").

1         	Cable 	: Enhanced IDE connector.

1         	Cable 	: F.D.D. connector.

1	Cable 	: Serial port.

1         	Cable 	: Serial/Parallel.

1         	Manual 	: User`s manual.

NOTE : Leave the mainboard in its original packing until you are ready to install it.

CHAPTER 2  INSTALLATION

2-1 INSTALLATION PROCEDURE

Before installing the computer, please prepare all components such as CPU, DRAM; peripherals such as hard disk drive, keyboard, CD-ROM drive; and accessories such as cables. Then, install the system as following .

1. Plug CPU (w/ heat sink and cooling fan), DRAM modules in the

mainboard.

2. Set jumpers based on your configuration.

3. Plug add-on cards in PCI or ISA slots.

4. Connect cables to peripherals, power supply..

5. Make sure all components and devices are well connected,

turn on the power and setup System BIOS based on your

configuration.

6. Install peripheral, add-on card drivers and test them.

7. If all of above procedures are success, turn-off the power then

plug all of them into your computer case.

2-2 CPU  INSTALLATION

ATC-2000 supports P54C and P55C types of CPUs up to 200MHz. For installation, please notice CPU pin 1 must align with the ZIF socket 7 Pin 1 location.

In the 2-2-1 describes the jumper setting for each brand of CPU. If your CPU is not in the list of 2-2-1, please refer to 2-2-2 and 2-2-3 for installation.

2-2-1 CPU TYPE SELECTION

A. INTEL PENTIUM CPU (P54C)

| JP10 | JP11 |  | 1-2 | 1-2 |  |
| --- | --- | --- | --- | --- | --- |

| CPU Core Voltage | VRE | STD |  | JP9 | 1-2 | 3-4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP7 | JP8 | JP3 | JP4 | Ext.x Frq. |  | 75MHz | close | close | 1-2 | 1-2 | 50x1.5 |  | 90MHz | open | close | 1-2 | 1-2 | 60x1.5 |  | 100MHz | close | open | 1-2 | 1-2 | 66x1.5 |  | 120MHz | open | close | 2-3 | 1-2 | 60x2.0 |  | 133MHz | close | open | 2-3 | 1-2 | 66x2.0 |  | 150MHz | open | close | 2-3 | 2-3 | 60x2.5 |  | 166MHz | close | open | 2-3 | 2-3 | 66x2.5 |  | 180MHz | open | close | 1-2 | 2-3 | 60x3.0 |  | 200MHz | close | open | 1-2 | 2-3 | 66x3.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

B. INTEL PENTIUM CPU (P55C)

Besides CPU clock setting, for P55C (MMX) CPU you have to set JP10/JP11based on its CPU I/O voltage type, and JP9 based on its core voltage.

| CPU Core Voltage | 2.8V* |  | JP9 | 7-8 |  |
| --- | --- | --- | --- | --- | --- |

*Currently, Intel P55C is released 2.8V core voltage only.

Please confirm this with your system supplier before you

install P55C CPU.

| I/O VOLTAGE | JP10 | JP11 |  | VI/O = 3.3V | 2-3 | 2-3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP7 | JP8 | JP3 | JP4 | Ext.x Frq. |  | 166MHz | close | open | 2-3 | 2-3 | 66x2.5 |  | 180MHz | open | close | 1-2 | 2-3 | 60x3.0 |  | 200MHz | close | open | 1-2 | 2-3 | 66x3.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

C. Cyrix 6x86 CPU

°¡Cyrix 6x86

| JP9 | JP10 | JP11 |  | 1-2 | 1-2 | 1-2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP7 | JP8 | JP3 | JP4 | Ext.x Frq. |  | PR120+ @ 100MHz | close | close | 2-3 | 1-2 | 50x2.0 |  | PR150+ @ 120MHz | open | close | 2-3 | 1-2 | 60x2.0 |  | PR166+ @ 133MHz | close | open | 2-3 | 1-2 | 66x2.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

°¡ Cyrix 6x86L CPU

| CPU | JP9 | JP10 | JP11 |  | Cyrix 6x86L | 7-8 | 2-3 | 2-3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP7 | JP8 | JP3 | JP4 | Ext.x Frq. |  | PR120+ @ 100MHz | close | close | 2-3 | 1-2 | 50x2.0 |  | PR133+ @ 110MHz | open | open | 2-3 | 1-2 | 55x2.0 |  | PR150+ @ 120MHz | open | close | 2-3 | 1-2 | 60x2.0 |  | PR166+ @ 133MHz | close | open | 2-3 | 1-2 | 66x2.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

D. AMD-K5 CPU

| JP9 | JP10 | JP11 |  | 1-2 | 1-2 | 1-2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP7 | JP8 | JP3 | JP4 | Ext.x Frq. |  | PR75ABR 75MHz | close | close | 1-2 | 1-2 | 50x1.5 |  | PR90ABQ 90MHz | open | close | 1-2 | 1-2 | 60x1.5 |  | PR100ABQ 100MHz | close | open | 1-2 | 1-2 | 66x1.5 |  | PR120ABQ 90MHz | open | close | 1-2 | 1-2 | 60x1.5 |  | PR133ABQ 100MHz | close | open | 1-2 | 1-2 | 66x1.5 |  | PR166ABQ | close | open | 2-3 | 2-3 | 66x2.5 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

E. AMD-K6 CPU

| JP9 | JP10 | JP11 |  | 5-6 | 2-3 | 2-3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

| INTERNAL CPU CLOCK | JP7 | JP8 | JP3 | JP4 | Ext.x Frq. |  | PR166 | close | open | 2-3 | 2-3 | 66x2.5 |  | PR200 | close | open | 1-2 | 2-3 | 66x3.0 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-2-2 CPU VOLTAGE SETTING

JP9 is used to various CPU core voltage types.

| CPU CORE VOLTAGE | JP9 |  | INTEL | STD | 3-4 |  | (P54C) | VRE | 1-2 |  | P55C | 2.8V | 7-8 |  | Cyrix | 6x86(028) | 1-2 |  | Cyrix | 6x86L | 7-8 |  | AMD | K5 | 1-2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-2-3 CPU CLOCK SETTING

The following setting is for CPU speed released later than 2-1-1.

| EXTERNAL CPU CLOCK | JP7 | JP8 |  | 50(MHz) | close | close |  | 55(MHz) | open | open |  | 60(MHz) | open | close |  | 66(MHz) | close | open |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

External

CPU Clock :

| INTERNAL CPU CLOCK | JP3 | JP4 |  | INTEL EXTERNAL CLOCK X 1.5 | 1-2 | 1-2 |  | INTEL EXTERNAL CLOCK X 2.0 | 2-3 | 1-2 |  | INTEL EXTERNAL CLOCK X 2.5 | 2-3 | 2-3 |  | INTEL EXTERNAL CLOCK X 3.0 | 1-2 | 2-3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-3 SYSTEM MEMORY INSTALLATION

ATC-2000 provides four 72-pin SIM sockets for system memory expansion from 4MB to 256MB. These four SIMs are arranged to two banks, Bank0 (SIM 1, 2) and Bank1(SIM 3, 4), please refer to page A. Each bank provides 64-bit wide data path.

The mainboard accepts Fast Page Mode DRAM, and EDO Mode (Extended Data Out) DRAM, with a speed at least 70 nanosecond. You should plug DRAM modules into two sockets (same bank) or four sockets at one time. Each pair of modules must be the same size, type, and speed; no matter single-side or double-side module. Please plug in Bank 0 firstly if you only have 2 modules. The mainboard supports mixing of EDO DRAM SIMMs with fast page

mode DRAM SIMMs among different banks; please plug EDO in Bank 0, if you only have 2 EDO modules.

If you install more than 64MB DRAM on ATC-2000, and would like to get more than 64MB cacheable size function, you should plug one 16K8 (or 32K8) TAG RAM into U16A socket, and change BIOS value of ‘L2 Cache Cacheable Size’ to ‘512MB’. ( refer to the screen of “CMOS SETUP UTILITY”.; page 32)

°¡ System Memory Combinations Options °¡

| BANK0 | BANK1 | Total Memory |  | SIM 1, 2 | SIM 3, 4 | SIM 1- 4 |  | 2MBx2 | - | 4MB |  | - | 2MBx2 | 4MB |  | 4MBx2 | - | 8MB |  | - | 4MBx2 | 8MB |  | 8MBx2 | - | 16MB |  | - | 8MBx2 | 16MB |  | 4MBx2 | 4MBx2 | 16MB |  | 4MBx2 | 8MBx2 | 24MB |  |  | - continue - |  |  | 8MBx2 | 4MBx2 | 24MB |  | 16MBx2 | - | 32MB |  | - | 16MBx2 | 32MB |  | 8MBx2 | 8MBx2 | 32MB |  | 4MBx2 | 16MBx2 | 40MB |  | 16MBx2 | 4MBx2 | 40MB |  | 8MBx2 | 16MBx2 | 48MB |  | 16MBx2 | 8MBx2 | 48MB |  | 32MBx2 | - | 64MB |  | - | 32MBx2 | 64MB |  | 16MBx2 | 16MBx2 | 64MB |  | 4MBx2 | 32MBx2 | 72MB |  | 32MBx2 | 4MBx2 | 72MB |  | 8MBx2 | 32MBx2 | 80MB |  | 32MBx2 | 8MBx2 | 80MB |  | 16MBx2 | 32MBx2 | 96MB |  | 32MBx2 | 16MBx2 | 96MB |  | 64MBx2 | - | 128MB |  | - | 64MBx2 | 128MB |  | 32MBx2 | 32MBx2 | 128MB |  | 4MBx2 | 64MBx2 | 136MB |  | 64MBx2 | 4MBx2 | 136MB |  | 8MBx2 | 64MBx2 | 144MB |  | 64MBx2 | 8MBx2 | 144MB |  | 16MBx2 | 64MBx2 | 160MB |  | 64MBx2 | 16MBx2 | 160MB |  | 32MBx2 | 64MBx2 | 192MB |  | 64MBx2 | 32MBx2 | 192MB |  | 64MBx2 | 64MBx2 | 256MB |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-4 SRAM  INSTALLATION

ATC-2000 is built-in 256KB or 512KB Sync. Pipeline Burst SRAM on board and provides a Sync. SRAM module in COAST slot for further expansion.  The maximum capacity is 512KB.

°¡ System Memory Combinations Options °¡

| SRAM TYPE | SRAM SIZE | DATA SRAM | TAG SRAM |  | Synchronous | 256KB | 32K32 x 2pcs | 16K8 or |  | on board* | 512KB | 64K32 x 2pcs | 32K8 x 1pcs |  | Synchronous module | 256KB | 32K32 x 2pcs |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

16K8 or

| 32K8 x 1pcs |  |
| --- | --- |

* on board DATA SRAM chips loaction are U24 and U25,

TAG SRAM chip location is U16.  U16A socket is used for DRAM installed more than 64MB.  (refer to 2-3)

°¡ Upgrade Procedure :

For upgrading your Sync. SRAM from 256KB to 512KB by using COAST Module, you should plug-in the KIT-256 module, then set JP1 to “open” ( disable the original TAG on board). You must use KIT-256 for upgrading your system to 512KB Sync. SRAM , please contact your system dealer about this information. It does not need

any BIOS value adjustments for upgrading the SRAM size.

| On Board TAG | JP1 |  | Disable | open |  | Enable | close |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

(If your module is without Tag RAM,

please set JP1 “close“)

2-5 OTHER JUMPERS AND

CONNECTORS  DESCRIPTION

The location of following jumpers please refer to page A.

| Jumper | Function | Remark |  | JP5 | CMOS |
| --- | --- | --- | --- | --- | --- |

open: Normal¯¡

| close: Clear CMOS |  | JP6 | ATBUS CLK |
| --- | --- | --- | --- |

open: PCI CLK/3 for external

CPU clock 50MHz

close: PCI CLK/4 for external

| CPU clock 60, 66MHz |  |
| --- | --- |

¯¡is default setting

The locations of following connectors are indicated in page A.

When you plug a cable into the following I/O connectors, you should have the pin 1 edge of the cable aligned with the pin 1 end of the connector.

CN8 : Speaker, Keyboard Lock, Reset, SMI,

Turbo LED, and IDE LED connectors.

J1 : CPU cooling fan connector. Wire with +12V

voltage (most likely red wire) must be plugged

into pin2, and GROUND wires (most likely

black wires) must be plugged into pin1 and/or

pin3. please confirm the wire color represtation

with your supplier.

CAUTION: Plug wire into wrong connector will

DAMAGE fan and mainboard.

IR1 : Infrared module connector.

CN9 : Universal Serial Bus connector, this is

used to connect USB devices through an

optional dual head cable with a iron plane.

KB1 : 5-pin AT style compatible keyboard

connector.

CN1 : PS/2 mouse connector, which is used to

connect an optional cable.

pin1 : data

pin2 : N/C

pin3 : GND

pin4 : VCC

pin5 : clock

pin6 : N/C

PW1 : +5 Voltage power supply connector.

CN2/3:COM1/2

CN2/CN3 : this two connectors are used to

connect serial port cables.

| pin | signal name |  | 1 | DCD |  | 2 | Serial In |  | 3 | Serial Out |  | 4 | DTR |  | 5 | GND |  | 6 | DSR |  | 7 | RTS |  | 8 | CTS |  | 9 | RI |  | 10 | N/C |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

CN4 : this connector is used to connect floppy

disk drive through cable.

| pin | signal | pin | signal |  | 2 | RWC- | 20 | STEP- |  | 4 | reserved | 22 | Write Data |  | 6 | FDEDIN | 24 | Write Gate |  | 8 | Index- | 26 | Track 00- |  | 10 | Motor EnableA- | 28 | Write Protect- |  | 12 | Drive Sele.B- | 30 | Read Data- |  | 14 | Drive Sele.A- | 32 | Side 1 Sele.- |  | 16 | Motor EnableB- | 34 | DisketteChange |  | 18 | DIR- |  |  |  | All of odd pins are ground |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

CN5: LPT

CN5 : this connector is used to connect parallel

port cable.

| pin | signal | pin | signal |  | 1 | STROBE- | 10 | ACK- |  | 2 | Data Bit 0 | 11 | BUSY |  | 3 | Data Bit 1 | 12 | PE |  | 4 | Data Bit 2 | 13 | SLCT |  | 5 | Data Bit 3 | 14 | Auto Feed- |  | 6 | Data Bit 4 | 15 | ERROR- |  | 7 | Data Bit 5 | 16 | INIT- |  | 8 | Data Bit 6 | 17 | SLCT IN- |  | 9 | Data Bit 7 | 26 | N/C |  | pin18 -- pin25 are ground |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

CN6/CN7 : this two connectors are used to connect

IDE devices through IDE cables, total 4 devices.

| pin | signal | pin | signal |  | 1 | Reset IDE | 21 | DDRQ0(1) |  | 2 | GND | 22 | GND |  | 3 | Host Data 7 | 23 | I/O Write- |  | 4 | Host Data 8 | 24 | GND |  | 5 | Host Data 6 | 25 | I/O Read- |  | 6 | Host Data 9 | 26 | GND |  | 7 | Host Data 5 | 27 | IORDY |  | 8 | Host Data 10 | 28 | N/C |  | 9 | Host Data 4 | 29 | DDAK0-(1)- |  | 10 | Host Data 11 | 30 | GND |  | 11 | Host Data 3 | 31 | IRQ14* |  | 12 | Host Data 12 | 32 | IOCS16- |  | 13 | Host Data 2 | 33 | Addr 1 |  | 14 | Host Data 13 | 34 | N/C |  | 15 | Host Data 1 | 35 | Addr 0 |  | 16 | Host Data 14 | 36 | Addr 2 |  | 17 | Host Data 0 | 37 | Chip Sele.1P- |  | 18 | Host Data 15 | 38 | Chip Sele 3P- |  | 19 | GND | 39 | Activity |  | 20 | Key | 40 | GND |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

2-6 IDE DRIVER INSTALLATION

The IDE driver installation procedure is printed on the label of diskette as following :

Setup for DOS/Windows :

1. Starting MS-Windows 3.1 (or 3.11)

2. Select Program Manager, "RUN" a file, then type "A:\setup.exe"

3. Exit MS-Windows, turn power off; then turn power on.

Setup for Windows 95 :

1. Starting Windows 95

2. Select “My Computer”; select “Control Panel”; select “System”;

then select “Device Manager”, “Hard Disk Controllers”.

3. Double-click to remove default driver program, restart computer.

4. Follow the instructions on your screen to install new IDE driver

we offer in the 3.5“ diskette

5. Exit Windows 95, turn power off; then turn power on.

°¡For more information, please refer to Windows 95 manual.

Make sure your HDD should follow ATA standard, and your CD-ROM drive should follow ATAPI standard. When you plug-in the IDE devices, please plug your first and second devices into IDE 1 port (Master then Slave), then plug third and forth devices into IDE 2 port. If you have CD-ROM drive, please set it behind hard disk devices as the last device. For example, if you have 2 HDDs and 1 CD-ROM drive, you should set HDD1 and HDD2 in IDE1 Master and Slave, set CD-ROM drive in IDE 2 Master. Some of the brands devices combination may not work under this sequence, you can try to re-arrange the device sequence and retry to run it, or contact your vendor.

CHAPTER 3  AWARD BIOS

SETUP

This chapter explains the system BIOS setup, and how to update new BIOS. All BIOS screens showed in the following pages are default values, your system dealer will set up these values according to your demand of computer.

ATC-2000 uses Flash ROM to make BIOS easier to be updated by the floppy disk-based program. and to committe Microsoft

Windows 95 plug & play feature.

°¡  JP5 Setting is for Update System BIOS

| open | NORMAL¯¡ |  | close | CLEAR CMOS |  |
| --- | --- | --- | --- | --- | --- |

¯¡is default setting

NOTE : If your mainboard is used

‘Benchmarq‘ battery, you

should clear CMOS under

powering on, otherwise the

‘clear’ will not work.

°¡  JP14 Setting is for Voltage of Flash ROM

| 1-2 | +12V |  | 2-3 | +5V |  |
| --- | --- | --- | --- | --- | --- |

3-1 UPDATE BIOS PROCEDURES

If the BIOS needs to be updated, it can be obtained on a diskette from your system supplier. The BIOS diskette includes 3 files:

“awdflash.exe”  --  BIOS update utility program

“awdflash.doc”

“(update BIOS filename with version number).rom”

The update procedures are as following:

Boot the system to DOS mode in a normal manner.

Insert the updated diskette to drive A (or B).

Change working directory to floppy drive, A or B, which contains the update BIOS diskette. --  Type “a:\” or “b:\”, “ENTER”.

Run the BIOS update utility  --  Type “awdflash”, “ENTER”.

Type “(update BIOS file name with version number).rom”, ENTER.

Type “N” when the screen displays the message : " Do you want to save BIOS (Y/N) ?".

Type “Y“ when the screen shows the message : " Are you sure to  program (Y/N) ?".

Follow instructions displayed on the screen.  DO NOT remove the update BIOS diskette from the floppy drive nor turn the system power off until the BIOS update is completed.

Exit the utility and turn the system power off, set JP5 to 'close' to clear the CMOS. After about 10 seconds, set JP5 to 'open' (remove the jumper cap ), become the normal status.

Turn the system power on and test your system working properly or not.

3-2  AWARD SYSTEM BIOS

CONFIGURATION SETUP

The following pages explain how to set up the system configuration (CMOS) under the AWARD BIOS. The SETUP program is stored in the Read-Only-Memory (ROM) on the mainboard. To do the SETUP procedure, press the <Del> key when the system is booting up. The following main menu will appear. Please select " STANDARD CMOS SETUP" to enter the next screen.

ROM PCI/ISA BIOS (2A59FA29)

CMOS SETUP UTILITY

AWARD SOFTWARE, INC.

| STANDARD CMOS SETUP | INTEGRATED PERIPHERALS |  | BIOS FEATURES SETUP | PASSWORD SETTING |  | CHIPSET FEATURES SETUP | IDE HDD AUTO DETECTION |  | POWER MANAGEMENT SETUP | SAVE & EXIT SETUP |  | PNP/PCI CONFIGURATION | EXIT WITHOUT SAVING |  | LOAD BIOS DEFAULTS |  |  |  |  |  | ESC: Quit | :Select Item |  | F10: Save & Exit Setup | (Shift) F2 : Change Color |  | Time, Date, Hard Disk Type ..... |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

The section on the bottom of the main menu explains how to control this screen.  The other one section displays the items highlighted in the list.

This screen records, some basic hardware information, and set the system clock and error handling. These records can be lost or corrupted if the on-board battery  is failed or  weak.

ROM PCI/ISA BIOS (2A59FA29)

CMOS SETUP UTILITY

AWARD SOFTWARE, INC.

| STANDARD CMOS SETUP | INTEGRATED PERIPHERALS |  | BIOS FEATURES SETUP | PASSWORD SETTING |  | CHIPSET FEATURES SETUP | IDE HDD AUTO DETECTION |  | POWER MANAGEMENT SETUP | SAVE & EXIT SETUP |  | PNP/PCI CONFIGURATION | EXIT WITHOUT SAVING |  | LOAD BIOS DEFAULTS |  |  |  |  |  | ESC: Quit | :Select Item |  | F10: Save & Exit Setup | (Shift) F2 : Change Color |  | Time, Date, Hard Disk Type ..... |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

ROM PCI/ISA BIOS (2A59FA29)

STANDARD CMOS SETUP

AWARD SOFTWARE, INC.

| Date (mm:dd:yy) : Fri, Jun 14 1996 |  |  | Time(hh:mm:ss) : 13 : 37 : 14 |  |  | HARD DISKS TYPE SIZE CYLS HEAD PRECOMP LANDZ SECTOR MODE |  | Primary Master : Auto 0 0 0 0 0 0 Auto |  | Primary Slave : None 0 0 0 0 0 0 ---- |  | Secondary Master : None 0 0 0 0 0 0 ----- |  | Secondary Slave : None 0 0 0 0 0 0 ---- |  |  |  |  | Drive A : 1.44M, 3.5 in. | Base Memory : 640K |  | Drive B : None | Extended memory : 7168K |  |  | Other Memory : 384K |  | Video : EGA/VGA | ------------------------------------------------ |  | Halt On: All Errors | Total Memory : 8192K |  | ESC : Quit :Select Item PU/PD/+/- : Modify |  | F1 : Help (Shift) F2 : Change Color |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Date	mm is month, dd is date, yy is year.

| date | from 1 to 31 |  | month | from Jan. to Dec. |  | year | from 1900 to 2099 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Time	hh is hour, mm is minute, ss is second.

| hh | from 0 to 23 (24-hour military -time) |  | mm | from 0 to 59 |  | ss | from 0 to 59 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Primary Master	These categories identify the types of 2 channels

Primary Slave	that have been installed in the computer. There

Secondary Master	are 45 predefined types and 4 user definable

Secondary Slave	types are for Enhanced IDE BIOS. Type 1 to 45

are predefined. Type ‘user’ is user-definable.

Press PgUp/PgDn to select a numbered hard

disk type or type the number and press<Enter>.

If you select ‘Auto’ BIOS will auto-detect the

HDD & CD-ROM Drive at the POST stage and

showing the IDE for HDD & CD-ROM Drive. If

you select ‘user’, you will need to know the

information listed below. Enter the information 		directly from the keyboard and press <Enter>. 		This information should be from your hard disk

vender or dealer. If the controller of HDD

interface is ESDI, the selection shall be ‘Type			1’; is SCSI, the selection shall be ‘None’.

If the device has not been installed select

‘NONE’ and press <Enter>.

| Type | drive type |  | SIZE | automatically adjusts |  | CYLS | number of cylinders |  | HEAD | number of heads |  | PRECOMP | write precom |  | LANDZ | landing zone |  | SECTOR | number of sectors |  | MODE | mode type |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Drive A	This category identifies the types of floppy disk

Drive B	drive A or drive B that have been installed in 			the computer.

| None | No floppy drive installed |  | 360K, 5.25 in | 5.25“ PC-type 360KB capacity |  | 1.2M, 5.25 in | 5.25“ AT-type 1.2MB capacity |  | 720K, 3.5 in | 3.5“ double-side 720KB capacity |  | 1.44M, 3.5 in | 3.5“ double-side 1.44MB capacity |  | 2.88M, 3.5 in | 3.5“ double-side 2.88MB capacity |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Video	This category selects the type of video adapter

used for the primary system monitor. Although

secondary monitors are supported, you do not

have to select the type in Setup.

Halt On	This category determines whether the computer

will stop if an error is detectd during power up.

| No errors | When the BIOS detects a non-fatal error the system will be stopped and you will be prompted |  | All errors | The system boot will not be stopped for any error that may be detected |  |
| --- | --- | --- | --- | --- | --- |

All, But

| Keyboard | The system boot will not stop for a keyboard error, it will stop for all other errors |  |
| --- | --- | --- |

All, But

Diskette

The system boot will not stop for a disk error, it will stop for all other errors

All, But

| Disk/Key | The system boot will not stop for a disk or keyboard error, it will stop for all other errors |  |
| --- | --- | --- |

Memory	This category is display-only which is determined

by POST (Power On Self Test) of the BIOS.

Base Memory  The value of the base memory

is typically 512K or 640K based on the memory

installed on the mainboard.

Extended Memory  How much extended

memory is present during the POST. This is

the amount of memory located above 1MB in

the CPU‘s memory address map.

Other Memory  This refers to the memory

located in the 640K to 1024K address space.

The BIOS is the most frequent user of this RAM

area since this is where it shadows RAM.

This screen is a list of system configuration options. Some of them are defaults required by the mainboard's design, others depend on the features of your  system.

ROM PCI/ISA BIOS (2A59FA29)

CMOS SETUP UTILITY

AWARD SOFTWARE, INC.

| STANDARD CMOS SETUP | INTEGRATED PERIPHERALS |  | BIOS FEATURES SETUP | PASSWORD SETTING |  | CHIPSET FEATURES SETUP | IDE HDD AUTO DETECTION |  | POWER MANAGEMENT SETUP | SAVE & EXIT SETUP |  | PNP/PCI CONFIGURATION | EXIT WITHOUT SAVING |  | LOAD BIOS DEFAULTS |  |  |  |  |  | ESC: Quit | :Select Item |  | F10: Save & Exit Setup | (Shift) F2 : Change Color |  | Virus, Protection, Boot Sequence |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

ROM PCI/ISA BIOS (2A59FA29)

BIOS FEATURES SETUP

AWARD SOFTWARE, INC.

| Virus Warning | : Disabled | Video BIOS Shadow | : Enabled |  | CPU Internal Cache | : Enabled | C8000-CBFFF Shadow | : Disabled |  | External Cache | : Enabled | CC000-CFFFF Shadow | : Disabled |  | Quick Power On Self Test | : Disabled | D0000-D3FFF Shadow | : Disabled |  | Boot Sequence | : A, C |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

D4000

# Text boxes

| -D7FFF Shadow | : Disabled |  | Swap Floppy Drive | : Disabled | D8000-DBFFF Shadow | : Disabled |  | Boot Up Floppy Seek | : Enabled | DC000-DFFFF Shadow | : Disabled |  | Boot Up NumLock Status | : On |  |  |  | Boot Up System Speed | : High |  |  |  | Gate A20 Option | : Fast |  |  |  | Typematic Rate Setting | : Disabled |  |  | Typematic Rate(Chars/Sec) | : 6 | Esc : Quit :Select Item |  | Typematic Delay(Msec) | : 250 | F1 : Help PU/PD/+/- : Modify |  | Security Option | : Setup | F5 : Old Values (SHIFT)F2 : Color |  | PS/2 mouse function control | : Enabled | F6 : Load BIOS Defaults |  | PCI/VGA Palette Snoop | : Disabled | F7 : Load Setup Defaults |  | OS/2 select for DRAM>64MB | : Non-OS2 |  |  | Report No FDD for WIN 95 | : No |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Virus Warning	When this item is enabled, the BIOS will

monitor the boot sector and partition table of the

hard disk drive for any attempt at modification.

If an attempt is made, the BIOS will halt the

system and the following error message will

appear. Ma