CMD Technology 
			       INSTALL.DOC


The purpose of INSTALL.INI file is to provide user configuration of the 
install program.  The INSTALL.INI file has several sections, each headed 
by a word enclosed in brackets.  The following is the list of sections in 
this file:

  [CSA64XX]
  [DosDriver Options]
  [DestinationDirs]
  [SourceDiskFiles]
  [SourceDisksNames]


The order of the sections is not important.  Each section is followed by a 
number of lines.  The syntax and meaning of each line is defined in the 
subsequent sections.

[CSA64XX] Section
-----------------
This section gives you an option to install different drivers for different
CSA-64XX controller cards in a system.  Each line in this section begins with 
a keyword followed by an equal sign.  Each keyword controls different ways 
the install program installs files on your system.  On the right hand side of 
each equal sign are values assigned to the keyword.  The order of these lines 
is not important.  The following is the list of all the keywords:


	DosDriver
	WindowsDriver
	NetwareDriver

DosDriver
---------
This option installs the DOS driver or skips DOS driver installation.  It 
has a value of YES, NO or a question mark.  If this keyword is not present 
or if it is commented out with a semi-colon in front of the line, then 
the DOS driver is installed.  If the value is a question mark, then the 
user is prompted before installing the DOS driver.

   examples:

	;install DOS driver
	DosDriver=YES

	  or

	;prompt the user for DOS driver installation
	DosDriver=?

	  or

	;skip DOS driver installation
	DosDriver=NO

	  or

	;install DOS driver
	;DosDriver=NO      


WindowsDriver
-------------
This option installs the Windows driver or skips Windows driver installation. 
It has a value of YES, NO or a question mark.  If this keyword is not 
present or if it is commented out with a semi-colon in front of the line, 
then the Windows driver is installed.  If the value is a question mark, then 
the user is prompted before installing the Windows driver.


   examples:

	;install Windows Driver
	WindowsDriver=YES

	  or

	;prompt the user for Windows driver installation
	WindowsDriver=?

	  or


	;skip Windows driver installation
	WindowsDriver=NO

	  or

	;install Windows driver
	;WindowsDriver=NO


NetwareDriver
-------------
This option installs the Netware driver or skips Netware driver installation.  
It has a value of YES, NO or a question mark.  If this keyword is not 
present or if it is commented out with a semi-colon in front of the line, 
then the Netware driver is installed.  If the value is a question mark, then 
the user is prompted before installing the Netware driver.


   examples:

	;Install Netware Driver
	NetwareDriver=YES

	  or

	;prompt the user for Netware driver installation
	NetwareDriver=?

	  or

	;Skip Netware Driver Installation
	NetwareDriver=NO

	  or

	;Install Netware Driver Installation
	;NetwareDriver=NO      


[DosDriver OPTIONS] Section
---------------------------
This section allows users to set command line parameters for the DOS driver.
Each line in this section begins with a keyword followed by an equal sign.
Each keyword adds one command line parameter to the driver.  On the right
side of each equal sign are values assigned to the keyword.  The order 
of these lines is not important.  The following is the list of all the 
keywords:

  LBA Mode
  Advanced Timing
  Local Bus Speed
  Secondary Drive
  Secondary Irq
  Other Options

If any of the above keywords or a whole section of a keyword is missing then
the corresponding parameter(s) will not be set.  If a semicolon ";" is placed
in front of a line then that line is ignored.  If the value on the right 
side is a question mark "?" or blank, the user will be prompted for the value
of that option during installation.  The following is the explanation of all 
the keywords used in this section:

Advanced Timing
---------------
This option sets the IDE drive timings.  The value on the right hand side 
of the equal sign can be a YES or NO or a question mark.  If the value is 
YES then the Local Bus speed is obtained from the option "Local Bus Speed" 
defined in the next paragraph.  If  the value is NO, it will skip the 
"Local Bus Speed" option even though it is present.  If it is a question 
mark, then the user is prompted for this option during installation.  If 
this keyword is not present at all, then it will not set any IDE drive timings.

  example:
      Advanced Timing=YES 
	  or
      Advanced Timing=NO
	  or
      Advanced Timing=?

Local Bus Speed
---------------
If the "Advanced Timing" option is selected, the local bus speed value will
be expected.  The user can type a value on the right hand side of the equal 
sign (Mhz) or a question mark if for interactive prompt.  This option is 
valid only if user selects YES for Advanced Timing option.  

  example:
      Local Bus Speed = 33Mhz
	or
      Local Bus Speed = 50Mhz
	or
      Local Bus Speed = ?

Secondary Drive
---------------
If the user has a drive connected to their secondary IDE port, the install 
program can be able to scan the drive(s) in that port. The user can put a 
YES or NO for this option.  If the value is YES, then the install program 
starts scanning the secondary IDE port without prompting the user 
before scanning.  The install program skips scanning the secondary 
channel if the value is NO.  If it is a question mark, then the user is 
prompted for this option during installation.

  example:
    Secondary Drive=Yes
	or
    Secondary Drive=NO
	or
    Secondary Drive=?
	or
    ;Secondary Drive= 

Secondary Irq
-------------
This option is valid only if "Secondary Drive" option is selected.  The
right hand side of the equal sign is the hardware interrupt number for the 
secondary channel.  

  example:
    Secondary Irq=14
      or
    Secondary Irq=?

LBA Mode
--------
This options stands for Logical Block Addressing mode.  It can be set to
ON or OFF.  If ON is selected then the install program sets the Logical 
Block Addressing Mode.  CHS mode is used if the value is OFF.

  example:
      LBA Mode=ON
	or
      LBA Mode=OFF
	or
      LBA Mode=?

[DestinationDirs] Section
-------------------------
This section lists the destination directories for copying driver files.
Each line in this section begins with a keyword followed by an equal sign.  
On the right hand side of each equal sign is the path of the destination
directory.  The order of these lines is not important.  The following is 
the list of all the keywords:

DosDriverFiles
Windows/WFWG 3.1x
NetwareDriverFiles

DosDriverFiles
--------------
The install program copies all the DOS driver(s) and utility files to
a directory on the user's hard disk.  The user can specify the path
on the right hand side of the equal sign or type a question mark.
If the path is specified in this option, then the user is not prompted 
during installation.  If a question mark is detected, the user will be 
prompted for the path.  If this keyword is not present at all, then 
the default directory "C:\QUICKCMD" will be created and the files will be
copied to that directory.

  example:

    DosDriverFiles=c:\IDE
	      or
    DosDriverFiles=30\IDE
	      or
    DosDriverFiles=?


Windows/WFWG 3.1x
-----------------
The install program installs the FastDisk driver only if the user
has Windows/WFWG 3.1x installed on the system. The value on the right
hand side of the equal sign must be the user's Windows/WFWG 3.1x directory
or it can be a question mark.  If it is a question mark, the user is prompted 
for the directory to install the driver.  If this keyword is not present, 
it is assumed that the user does not have Windows/WFWG 3.1x installed in the 
system.

  example:

    Windows/WFWG 3.1x=c:\windows
	      or
    Windows/WFWG 3.1x=?
	      or
    ;Windows/WFWG 3.1x=


NetwareDriverFiles
------------------
The install program installs the netware driver if the system will be
used as a Novell Netware 3.1x server.  The value on the right hand side of 
the equal sign must be the directory where the Netware Drivers will be
installed.  If it is a question mark, then the user is prompted for this 
options during installation.  If this keyword is not present at all, then
it is assumed that the user will not use the system for Novell Netware 3.1x
server.

  example:
    NetwareDriverFiles=c:\netware
	  or
    ;NetwareDriverFiles=c:\netware


SourceDisksFiles Section
-----------------------
This sections lists all the source files required for the installation.
All the entries in this section have the following syntax:

SourceFileName,DiskNumber,SourceFilePath

example:

	CMD646X.PCI,1,DOS\PCI
	CHECKIDE.EXE,1,DOS
	
SourceDisksNames Section
------------------------
This section provides information required by the "SourceDisksFiles" section.
It contains the information regarding each of the disks that are used in the 
installation.

DiskNumber="Disk Description", DiskLabel

example:

	1="CMD 646x Install Disk"," Disk#1"