CB60-ZX Intel® 440ZX-100 Celeron™ PPGA Processor ATX System Board ESSOR

300A/333/366/400/433MHz and future 100MHz FSB Celeron™ PPGA processor

Intel® 440ZX-100 AGP set

8MB to 256MB memory using unbuffered DIMMs

Two 168-pin DIMM sockets

Uses x64 PC SDRAM, 3.3V PC-66 SDRAM DIMM for 66MHz FSB processors PC-100 SDRAM DIMM for 100MHz FSB processors

ECC supported (uses x72 PC SDRAM DIMM)

Award BIOS, Windows® 95 Plug and Play compatible

Flash EPROM for easy BIOS upgrades (2MB)

Supports DMI 2.0 function.

ENERGY EFFICIENT DESIGN

Supports ACPI specification and OS Directed Power Management

Wake-On-Events include: RTC timer to power-on the system Modem ring-on Wake-On-LAN Wake-On-keyboard/Wake-On-Mouse

System power management supported

CPU stopped clock control

Hardware supports SMI green mode

Microsoft®/Intel® APM 1.2 compliant

Soft Power supported - ACPI v1.0a specification

AC power failure recovery

Monitors processor/system temperature and processor overheat alarm

Monitors 1.5V/3.3V/±5V/±12V/VCORE voltages and failure alarm

Monitors processor/system fan speed and failure alarm

Automatic processor fan control to save energy, prevent system overheat, prolong fan life and implement silent system.

Three types of sound for different failure alarm

Read back capability that displays temperature, voltage and fan speed

Ultra DMA/33 supported (Synchronous DMA mode -data transfer rate up to 33MB/sec.)

PIO Mode 3 and Mode 4 Enhanced IDE (data transfer rate up to 16.6MB/sec.)

Bus mastering reduces CPU utilization during disk transfer

ATAPI CD-ROM, LS-120 and ZIP supported

Two NS16C550A-compatible high speed UARTs

One SPP/ECP/EPP parallel port

Supports up to 2.88MB floppy drives

Intel® Socket 370

Equipped with a switching voltage regulator that automatically detects 1.30V to 2.05V

AGP is an interface designed to support high performance 3D graphics cards

Supports up to 533MB/sec. bandwidth for 3D graphics applications

2 USB ports

2 DB-9 serial ports

1 DB-25 parallel port

1 mini-DIN-6 PS/2 mouse port

1 mini-DIN-6 PS/2 keyboard port

1 connector for IrDA interface

2 IDE connectors

1 floppy connector

1 20-pin ATX power supply connector

1 3-pin WOL (Wake-ON-Lan) connector

1 SB-LINK connector

3 fan connectors for CPU, chassis and AGP fans

1 dedicated AGP slot

3 dedicated PCI slot

2 dedicated 16-bit ISA slots

1 shared PCI/ISA slot

4 layers, ATX form factor

30.48cm (12") x 17.2cm (6.67")