P2XBL/D
Supports Intel® Pentium III Processor 500MHz
Intel® 440BX Pentium® II Dual Processor

Features

| Dual Intel® Slot 1 processor slot |  |
| --- | --- |
| Accelerated Graphics Port (AGP) with up to 533MB/sec. bandwidth |  |
| Supports ACPI specification |  |
| Supports modem ring-on and RTC timer to power-on the system |  |
| Supports Wake-On-LAN function |  |
| Monitors processor/system temperature, power voltages, processor/system fan speed and fan on/off control |  |
| EC and ECC supported |  |

Specifications

PROCESSOR

233/66MHz Pentium® II processor

266/66MHz Pentium® II processor

300/66MHz Pentium® II processor

333/66MHz Pentium® II processor

350/100MHz Pentium® II processor

400/100MHz Pentium® II processor

450/100MHz Pentium® II processor

333MHz Celeron™ processor

Intel® 440BX AGP set

SYSTEM MEMORY

8MB to 512MB using unbuffered DIMMs

8MB to 1GB using registered DIMMs

Four 168-pin DIMM sockets

Uses x64 or x72 SDRAM DIMM, 3.3V PC/66 SDRAM DIMM for 66MHz FSB PC/100 SDRAM DIMM for 100MHz FSB

EC and ECC supported (uses x72 SDRAM DIMM)

BIOS

Award BIOS, Windows® 95 Plug and Play compatible

Flash EPROM for easy BIOS upgrades

Includes NCR 810 SCSI BIOS

Supports DMI 2.0 function

ENERGY EFFICIENT DESIGN

Supports ACPI specification and OS Directed Power Management

RTC timer to power on or wake-up the system

Modem Ring-On/Wake-Up

Wake-On-Lan ready

System power management supported

CPU stopped clock control

Hardware supports SMI green mode

Microsoft®/Intel® APM 1.2 compliant

Soft Power supported - ACPI v1.0a specification

DAMAGE FREE INTELLIGENCE

Monitors processor/system temperature and overheat alarm

Monitors +3.3V/±5V/±12V voltages and failure alarm

Monitors processor/system fan speed and failure alarm

Automatic processor fan control to save energy, prevent system overheat, prolong fan life and implement silent system

Three types of sound for different failure alarm

Read back capability that displays accurate temperature, voltage and fan speed

PCI IDE INTERFACE

Ultra DMA/33 supported (Synchronous DMA mode - data transfer rate up to 33MB/sec.)

PIO Mode 3 and Mode 4 Enhanced IDE (data transfer rate up to 16.6MB/sec.)

Bus mastering reduces CPU utilization during disk transfer

ATAPI CD-ROM supported

LS-120 and ZIP supported

INTEGRATED I/O

Two NS16C550A-compatible high speed UARTs

One SPP/ECP/EPP parallel port

Support up to 2.88MB floppy drivers

PROCESSOR SLOT

Dual Intel® Slot 1 connector(242-pin processor slot)

Equipped with a switching voltage regulator that automatically detects 1.8V to 3.5V

ACCELERATED GRAPHICS PORT (A.G.)

AGP is an interface designed to support high performance 3D graphics cards

Supports up to 533MB/sec. bandwidth for 3D graphics applications

ATX DOUBLE DECK PORTS

2 USB ports

2 DB-9 serial ports

1 DB-25 parallel port

1 mini-DIN-6 PS/2 keyboard port

1 mini-DIN-6 PS/2 mouse port

NNECTORS

1connector for IrDA interface

2 IDE connectors

1 floppy connector

1 20-pin ATX power supply connector

1 3-pin WOL (Wake-ON-Lan) connector

1 SB-Link connector

EXPANSION SLOTS

1 dedicated AGP slot

3 dedicated PCI slot

2 dedicated 16-bit ISA slots

1 shared PCI/ISA slot

PCB

4 layers, ATX form factor

30.48cm (12") x 24.5cm (9.64")