PB50-ZX
Intel® 4440ZX-100 Pentium® II Processor Baby AT System Board

PROCESSOR

233/66MHz, 266/66MHz, 300/66MHz, 333/66MHz, 350/100MHz, 400/100MHz, 450/100MHz or 500/100MHz Pentium® II processor

266/300/300A/333/366MHz Celeron™ processor

Intel® 440ZX-100 AGP set

8MB to 256MB memory using unbuffered DIMMs

Two 168-pin DIMM sockets

Uses x64 PC SDRAM, 3.3V PC-66 SDRAM DIMM for 66MHz FSB processors PC-100 SDRAM DIMM for 100MHz FSB processors

ECC supported (uses x72 PC SDRAM DIMM)

Award BIOS, Windows® 95 Plug and Play compatible

Flash EPROM for easy BIOS upgrades (2MB)

Supports DMI 2.0 function

Supports ACPI specification and OS Directed Power Management(ATX power supply only)

Wake-On-Events include(ATX power supply only): RTC timer to power-on the system Modem ring-on Wake-On-LAN Wake-On-keyboard/Wake-On-Mouse

System power management supported

CPU stopped clock control

Hardware supports SMI green mode

Microsoft®/Intel® APM 1.2 compliant

Soft Power supported - ACPI v1.0a specification(ATX power supply only)

AC power failure recovery

DAMAGE FREE INTELLIGENCE

Monitors processor/system temperature and processor overheat alarm

Monitors 1.5V/3.3V/±5V/±12V/VCORE voltages and failure alarm

Monitors processor/system fan speed and failure alarm

Automatic processor fan control to save energy, prevent system overheat, prolong fan life and implement silent system

Read back capability that displays temperature, voltage and fan speed

Ultra DMA/33 supported (Synchronous DMA mode -data transfer rate up to 33MB/sec.)

PIO Mode 3 and Mode 4 Enhanced IDE (data transfer rate up to 16.6MB/sec.)

Bus mastering reduces CPU utilization during disk transfer

ATAPI CD-ROM, LS-120 and ZIP supported

Two NS16C550A-compatible high speed UARTs

One SPP/ECP/EPP parallel port

Supports up to 2.88MB floppy drives

Intel® Slot 1 connector (242-pin processor slot)

Equipped with a switching voltage regulator that automatically detects 1.30V to 3.5V

AGP is an interface designed to support high performance 3D graphics cards

Supports up to 533MB/sec. bandwidth for 3D graphics applications

2 connectors for external USB ports

1 connector for IrDA interface

2 serial ports

1 parallel port

2 IDE connectors

1 floppy connector

1 PS/2 mouse port

1 PS/2 or AT keyboard port

1 20-pin ATX power supply connector

1 12-pin standard AT power supply connector

1 Wake-on-LAN connector

1 SB-LINK connector

3 fan connectors for CPU, chassis and AGP fans

1 dedicated AGP slot

3 dedicated PCI slot

2 dedicated 16-bit ISA slots

1 shared PCI/ISA slot

4 layers, Baby AT form factor

26.5cm (10.43") x 22.4cm (8.82")