Trinity ATX (S1592) Quick Setup Guide

|  | The table below will help you set the jumpers for CPU speed, bus frequency, and memory voltage,among others. * This motherboard incorporates support for 75 MHz and 83 MHz BUS speeds. However, these speeds will push PCI bandwidth beyond the Intel recommended specification for PCI 2.1 compliance. Therefore, TYAN Computer Corporation takes no responsibility for any problems, be it hardware or software, related to the use of BUS speeds beyond 66MHz. We also cannot guarantee any PCI cards' compatibility beyond the specified speed of 33MHz. Technical support and RMA / Warranty claims relating to the use of BUS speeds beyond the 66 MHz / 33 MHz limit recommended by Intel will not be honored by TYAN. USE AT YOUR OWN RISK. ** The JPW1 setting for the Cyrix 6x86L series will vary. Some of the CPUs in this series are 2.8V, and others are 3.3V. Check the face of the CPU and the CPU Voltage Settings table for the proper settings for these jumpers. |
| --- | --- |

|  | Trinity Jumper Settings by CPU Type - Updated 7-14-98 |
| --- | --- |

|  | CPU BUS Speed & Multiplier JP3 JP4 JP5 JPW1 1-2 JPW1 3-4 JPW1 5-6 JPW1 7-8 JP10 JP11 JP12 Intel P54C 75 50MHz x 1.5 OFF OFF OFF ON OFF ON ON 2-3 2-3 2-3 Intel P54C 90 60MHz x 1.5 OFF OFF OFF ON OFF ON ON 2-3 1-2 1-2 Intel P54C 100 66MHz x 1.5 OFF OFF OFF ON OFF ON ON 1-2 1-2 1-2 Intel P54C 120 60MHz x 2 OFF OFF ON ON OFF ON ON 2-3 1-2 1-2 Intel P54C 133 66MHz x 2 OFF OFF ON ON OFF ON ON 1-2 1-2 1-2 Intel P54C 150 60MHz x 2.5 OFF ON ON ON OFF ON ON 2-3 1-2 1-2 Intel P54C 166 66MHz x 2.5 OFF ON ON ON OFF ON ON 1-2 1-2 1-2 Intel P54C 200 66MHz x 3 OFF ON OFF ON OFF ON ON 1-2 1-2 1-2 Intel P55C 166 MMX 66MHz x 2.5 OFF ON ON OFF OFF OFF ON 1-2 1-2 1-2 Intel P55C 200 MMX 66MHz x 3 OFF ON OFF OFF OFF OFF ON 1-2 1-2 1-2 Intel P55C 233 MMX 66MHz x 3.5 OFF OFF OFF OFF OFF OFF ON 1-2 1-2 1-2 AMD K5 100 66MHz X 1.5 OFF OFF OFF ON OFF ON ON 1-2 1-2 1-2 AMD K5 120 60MHz x 2 OFF OFF ON ON OFF ON ON 2-3 1-2 1-2 AMD K5 133 66MHz x 2 OFF OFF ON ON OFF ON ON 1-2 1-2 1-2 AMD K5 166 66MHz x 2.5 OFF ON ON ON OFF ON ON 1-2 1-2 1-2 AMD K6 166 66MHz x 2.5 OFF ON ON ON OFF OFF ON 1-2 1-2 1-2 AMD K6 200 66MHz x 3 OFF ON OFF ON OFF OFF ON 1-2 1-2 1-2 AMD K6 233 66MHz x 3.5 OFF OFF OFF OFF ON OFF OFF 1-2 1-2 1-2 AMD K6 266 66MHz x 4 ON OFF ON OFF ON OFF OFF 1-2 1-2 1-2 IDT C6 180 60MHz x 3 OFF ON OFF ON OFF ON ON 2-3 1-2 1-2 IDT C6 200 66MHz x 3.5 OFF ON OFF ON OFF ON ON 1-2 1-2 1-2 Cyrix PR120+ 6x86 50MHz x 2 OFF OFF ON ON OFF ON ON 2-3 2-3 2-3 Cyrix PR150+ 6x86 60MHz x 2 OFF OFF ON ON OFF ON ON 2-3 1-2 1-2 Cyrix PR166+ 6x86 66MHz x 2 OFF OFF ON ON OFF ON ON 1-2 1-2 1-2 Cyrix PR200+ 6x86 75MHz x 2* OFF OFF ON ON OFF ON ON 1-2 2-3 1-2 Cyrix PR150+ 6x86L** 60MHz x 2 OFF OFF ON OFF OFF OFF ON 2-3 1-2 1-2 Cyrix PR166+ 6x86L** 66MHz x 2 OFF OFF ON OFF OFF OFF ON 1-2 1-2 1-2 Cyrix PR200+ 6x86L** 75MHz x 2* OFF OFF ON OFF OFF OFF ON 1-2 2-3 1-2 Cyrix PR166+ 6x86MX 60MHz x 2.5 OFF ON ON ON OFF OFF ON 2-3 1-2 1-2 Cyrix PR166+ 6x86MX 66MHz x 2 OFF OFF ON ON OFF OFF ON 1-2 1-2 1-2 Cyrix PR200+ 6x86MX 66MHz x 2.5 OFF ON ON ON OFF OFF ON 1-2 1-2 1-2 Cyrix PR200+ 6x86MX 75MHz x 2* OFF OFF ON ON OFF OFF ON 1-2 2-3 1-2 Cyrix PR200+ 6x86MX 66MHz x 3 OFF ON OFF ON OFF OFF ON 1-2 1-2 1-2 Cyrix PR233+ 6x86MX 75MHz x 2.5* OFF ON ON ON OFF OFF ON 1-2 2-3 1-2 |
| --- | --- |

© Copyright 2001, Tyan Computer Corporation. All Rights Reserved.